## Slide 1: Luganda voice-controlled wheelchair project
Project progress
Samuel and Adi

## Slide 2: Recap
The main objective is to develop a Luganda voice-controlled wheelchair system
Specific objectives
To collect and curate a Luganda voice dataset for common wheelchair movement commands.
To develop, train and evaluate a speech intent recognition model to classify spoken Luganda commands.
To integrate the trained model with a wheelchair to form a voice-controlled wheelchair system.
To evaluate the system.

## Slide 3: Work completed
Reading the literature review of the existing systems
Determining the hardware components to use for the project
Getting a google dataset to use to train an English version of the model
Getting the commands to use for the project
The wake word to use in the project

## Slide 4: Commands
Command in English | Command in Luganda
Wake word | Gaali
Forward | mu maaso
Backward | okudda emabega
Stop | okuyimirira
Right | omukono ogwa ddyo
Left | kkono

## Slide 5: Hardware components
Boards
Microphone
Motor driver
Motors
Speakers

## Slide 6: Deployment
ESp32
Deploying the wake word on the ESP32 board
Raspberry Pi
Deploying the speech intent model

## Slide 7: Speakers
reSpeaker 2-Mics Pi HAT
Has 4 analogue microphones
Voice Interaction algorithms of VAD(Voice Activity Detection), DOA(Direction of Arrival), KWS(Key Word Spotting)
WM8960 Audio Codec: Low power, high-quality stereo Codec
Controllable Peripherals: Provide 3 programable APAI 02 RGB LEDs and 1 User Button for attached Speech
Recognition usage
Mems Microphone Module with12C
High Precision & performance
low-power
digital output
Direct connection to board
High signal-to-noise ratio
wideband frequency response

## Slide 8: Motor Driver
L298N Motor Driver Board
Is a high voltage and high current dual full-bridge
driver it can up to 46V and Dc current up to 4amp controlling motors is needed from microcontrollers, switches, relays.
can control up to 4 DC motors, or 2 DC motors with direction and speed control

## Slide 9: Motor
G12-N20 Geared Mini DC Motor
Medium Power MP: 0.5W Max.
Rated Voltage: 6~12V.
5V -12V
300 RPM
Brushed contacts.
Relatively Cheap

## Slide 10
Logic flow

## Slide 11: Current status
Still doing literature review
Pending training of the English model
Making slides for the proposal presentations

## Slide 12: Upcoming tasks
Purchasing the hardware
Initial testing of the hardware